## Slide 1
VIT • BITE305L COURSE PROJECT
RIP vs OSPF Routing Protocol Performance
Cisco Packet Tracer + Python Streamlit Dashboard
Implementation demonstration • experimental evidence to be collected in Packet Tracer

## Slide 2
The problem we are solving
Why do we compare dynamic routing?
BITE305L • COMPUTER NETWORKS • RIP vs OSPF
Link failures
Communication may stop when the preferred router-to-router link becomes unavailable.
Different route metrics
RIPv2 prioritizes hop count, while OSPF uses accumulated interface cost.
Need for objective evidence
We need identical topologies and repeatable experiments to compare recovery behavior.

## Slide 3
Network architecture
5 routers • 2 switches • 2 end devices
BITE305L • COMPUTER NETWORKS • RIP vs OSPF
Upper route: 2 hops | Lower route: 3 hops | Controlled link: R2 – R4

## Slide 4
How the two protocols differ
Two protocols, one controlled topology
BITE305L • COMPUTER NETWORKS • RIP vs OSPF
RIPv2
Distance vector Advertises routes to neighbors Metric: hop count Hop-minimal expected route
OSPFv2
Link state Shortest-path-first computation Metric: sum of interface costs Can favor a longer-hop path
This project compares protocols; it does not invent a new routing algorithm.

## Slide 5
Experiment scenarios
Paired tests for RIP and OSPF
BITE305L • COMPUTER NETWORKS • RIP vs OSPF
01
Baseline
Confirm initial route and connectivity
02
Failure
Shutdown R2 Gi0/1; check backup route
03
Restoration
Restore R2–R4 and observe preferred route
04
Cost demonstration
OSPF upper cost 100 vs lower cost 10

## Slide 6
Python dashboard
Six screens turn configuration into an explainable experiment
BITE305L • COMPUTER NETWORKS • RIP vs OSPF
Overview
Problem and objectives
Topology
Calculated expected routes
Experiments
CLI commands and methodology
Measurements
CSV validation and charts
Algorithms
BFS/Dijkstra calculation trace
Submission
Evidence checklist

## Slide 7
Results: evidence first
No fabricated convergence-time or packet-loss numbers
BITE305L • COMPUTER NETWORKS • RIP vs OSPF
Observed results are entered through a CSV worksheet.
Required evidence: route tables, failed-link transitions, recovered routes, ICMP counts, and clearly defined timing basis. The dashboard generates charts only after data is recorded.
Important: Packet Tracer paths must be tested on a real Packet Tracer installation.

## Slide 8
What is already built vs still required
Clear completion status for the final demonstration
BITE305L • COMPUTER NETWORKS • RIP vs OSPF
IMPLEMENTED
• 5-router IP plan and CLI configs • Separate RIP/OSPF config sets • Streamlit dashboard source • Routing model with unit tests • Blank CSV + report draft
REQUIRES PACKET TRACER
• Save and verify both .pkt files • Execute 3 matched test runs • Capture real screenshots • Record actual metric values • Verify 15 recent papers